## Slide 1: VyOS: Network Operating System
Introduction and Quick Start Workshop

## Slide 2: Mehdi Sarmadi
Professional Life
  Open Source Consultant/Enthusiast
  14 years of Linux/OpenSource Journey
  Data Center Service Consultant/Project Manager
  Identity and Access Management Architect
  HPC Architect
  Performance Engineering
  Product Design
  CTO of Aris System
https://github.com/msarmadi/vyos-workshop-2015
msarmadi@gmail.com

## Slide 3: The Story
نیروی انسانی متخصص
بازار کار تخصصی
آموزش و مدارک حرفه ای
  شبکه ها (CISCO، Juniper، Mikrotik، F5، Palo Alto، Check Point...)
  برنامه سازی (Java, PPP، RUP، Scrum، AUP، ...)
  پایگاه داده (Oracle DB، MS SQL Server)
  مدیریت سیستم (MS Windows، VMWare VI، Linux، Solaris)
  تجهیزات پردازشی، ذخیره سازی، .. (HP، EMC، IBM، DELL)
  امنیت (.....)

## Slide 6: To Be In Control or Under Control

## Slide 7: Traditional Networking vs New Vision
Hardware Focused
  CISCO,
  Juniper,
  Extreme,
  Brocade,
  Alcatel-Lucent, …
General Hardware and Software Focused
  Vyatta
  VyOS
  EdgeOS
  …

## Slide 8: Proven
Open Source Software
with Active Community/Support
Leads to
Acceleration & Quality

## Slide 13: Vyatta Advantage
Most widely deployed vRouter in the world
10x Cisco’s throughput
Supports all major hypervisors
Linux Based
Restful APIs
Benchmark (2/25/13)
Cisco CSR 1000v Vyatta
HW: Cores 4 cores 1 core
HW: Type New Any
Throughput 50 Mbps 500 Mbps

## Slide 14: Single, Integrated Product
vRouter
Next Generation
Cloud (Multi Tenancy, Hybrid, Virtual)
SDN (Software Defined Network)
NFV (Network Function Virtualization)
Router
Firewall
VPN
OSPF, BGP
Stateful, NAT
IPSec, SSL

## Slide 15: Router Highlights
Routing
Security
VPN
System Management
IP Services
Platforms
High Availability
IPv4, IPv6, Static, PBR, OSPF, RIP, BGP
IPv4, IPv6, Stateful Firewall, NAT, Zone Based Firewall
IPSec, SSL, Route-based, L2-bridging
CLI, REST API, GUI
SSH, DHCP, DNS, SNMP
VRRP, Stateful Failover, Config Sync
VMware, Xen, KVM, Hyper-V, x86
Notes: Read through each block: To highlight Vyatta’s breadth, this slide reflects our standards based approach to provide routing (protocols such as BGP, OSPF, RIP…), from a security perspective, we provide stateful firewall, VPN (IPSEC and OPENVPN); threat protection (traffic and web filtering), system management, IP Services in high availability across standard platforms…
(SALES FOLKS: this slide is features and benefits, it is a high level representation of our system, just highlight the ones you know or that make your presentation flow, do not read this slide!)….

## Slide 16: 2013: Brocade Acquired/Killed Vyatta in

## Slide 17: Dead? - Not Totally
2013 - VyOS born
A community fork of the GPL portions of Vyatta Core 6.6R1
Open Source – Committed to Debian Social Commitment
Minimal Features – To make it manageable
Japanese User Group, Universities/Coporates
Debian 6.0 Squeeze

## Slide 21
Architecture
Linux Kernel with Multi-Platform Virtualization Drivers
Routing
Firewall
NAT
VPN
QoS
IPv6
Data Model
CLI
API
GUI

## Slide 22: VyOS
Not a SOHO (like D-Link, Linksys, …): you should know what you do
A world class router/VPN/firewall
  Personal, Business Use – e.g. Site to Site IPSEC, Cloud to Cloud Bridge
  Replacement: EdgeOS, pfSense, Cisco ASA/Routers, Cisco v1000
  Research: use it as a serious Router/Firewall add your function & benchmark
Contribution Ideas
  WebUI / Core Features / Network Courses / e.g. TCPCrypt Socket Encryption

## Slide 23: Resources and References
Project Goals http://vyos.net/wiki/Project_Goals
Blog http://blog.vyos.net/
WebSite http://vyos.net/
GitHub http://github.com/vyos/
WiKi http://vyos.net/wiki
FAQ http://vyos.net/wiki/FAQ
vBuddy http://www.vyatta4people.org/ , http://blog.cyberlynx.eu/

## Slide 24: Hardware Resource
 | Disk | RAM
Minimum | 2GB | 128MB
Recommended | 3GB or more based on usage (if you have cache or need image upgrade) | 512MB or more Based on usage (high concurrency on nat, cache, vpn, …)

## Slide 25: Releases
Hydrogen is 1.0 – First Major Release (Late 2013)
  http://vyos.net/wiki/Hydrogen
Helium 1.1.0 (Summer 2014)
  http://vyos.net/wiki/Helium
Lithium 1.2.0 (Spring 2015)
  http://vyos.net/wiki/Lithium

## Slide 26: Workshop
Live Mode
Installation
CLI Concepts
  Configuration Mode/Commit/Rollback/Save/Show Info/exit, exit discard, description
  TAB & Abbreviation
Initialization
  Set and Show : Hostname, IP address, Gateway, DNS, SSH, User
Basics
  Configuration: Set/Edit/commit-confirm/confirm/compare/discard
  /history/show & monitor log/ | commands
Configuration Scenarios
  NAT / Web Cache / VPN Server / Firewall Rules
Hacks
  FS Layout, Build ISO, vbash, add new commands, vbuddy, install debian packages

## Slide 27: Install & CLI
Login: vyos / vyos
Install:
  install image
  reboot
CLI
  s[tab]
  show [tab]
    [q] quit
    [space] page down
    [b] page up
  configure, exit

## Slide 28: CLI Concepts
show configuration
show configuration commands
configure
  show interfaces
  set interfaces ethernet eth0 description 'OUTSIDE‘
  show interfaces
  delete interfaces ethernet eth0 description 'OUTSIDE
  changes
  commit
  discard
  exit
  exit discard

## Slide 29: Basic Setup
IP Address
  Static
    set interface ethernet eth0 address 192.168.1.123/24
  DHCP
    set interfaces ethernet eth0 description 'OUTSIDE'
    set interfaces ethernet eth0 address 'dhcp'
SSH
  set service ssh port ‘22’
  set service ssh listen-address 192.168.1.123

## Slide 30: Basic Setup
Gateway
  set system gateway-address '192.168.22.254'
Hostname
  set system host-name 'vyos‘
DNS (required for web proxy)
  set system name-server '192.168.22.253'

## Slide 31: Static Route
set protocols static route 192.168.113.0/24 next-hop 172.20.13.1 distance ‘1‘

## Slide 32: DNS Forwarder
set service dns forwarding cache-size ‘0‘
set service dns forwarding listen-on 'eth1‘
set service dns forwarding name-server '8.8.8.8'

## Slide 33: NAT
Masquerade
  set nat source rule 100 outbound-interface 'eth0'
  set nat source rule 100 source address '192.168.1.0/24'
  set nat source rule 100 translation address 'masquerade‘
DNAT
  set nat destination rule 10 description 'Port Forward: HTTP to 192.168.0.100'
  set nat destination rule 10 destination port '80'
  set nat destination rule 10 inbound-interface 'eth0'
  set nat destination rule 10 protocol 'tcp'
  set nat destination rule 10 translation address '192.168.0.100'

## Slide 34: Bridging
Bridging
  set interfaces bridge 'br100'
  set interfaces ethernet eth1 vif 100
  bridge-group bridge br100
  set interfaces bridge br100 address '192.168.100.1/24‘
  set interfaces bridge br100 stp true
  show bridge
  show bridge br100 spanning-tree

## Slide 35: Setup a DHCP Server
set service dhcp-server disabled ‘false‘
set service dhcp-server shared-network-name LAN subnet 192.168.0.0/24 default-router ‘192.168.0.1‘
set service dhcp-server shared-network-name LAN subnet 192.168.0.0/24 dns-server ‘192.168.0.1‘
set service dhcp-server shared-network-name LAN subnet 192.168.0.0/24 domain-name ‘internal-network
set service dhcp-server shared-network-name LAN subnet 192.168.0.0/24 lease ‘86400‘
set service dhcp-server shared-network-name LAN subnet 192.168.0.0/24 start 192.168.0.9 stop ‘192.168.0.254'

## Slide 36: Setup Web Proxy
Turn on
  set service webproxy listen-address 192.168.0.1
  set service webproxy listen-address 192.168.0.1 port 3128
  set service webproxy listen-address 192.168.0.1 disable-transparent
Cache
  set service webproxy cache-size 100
URL Filter
  set service webproxy url-filtering squidguard local-block google.com
  set service webproxy url-filtering squidguard log local-block

## Slide 37: Resources and References
Project Goals http://vyos.net/wiki/Project_Goals
Blog http://blog.vyos.net/
WebSite http://vyos.net/
GitHub http://github.com/vyos/
WiKi http://vyos.net/wiki
FAQ http://vyos.net/wiki/FAQ
vBuddy http://www.vyatta4people.org/ , http://blog.cyberlynx.eu/

## Slide 38: Advanced Scenarios using Vyos/vyatta
Even DMVPN

## Slide 39: Cloud Bridging
Full mesh VPN between multiple VPCs and datacenter
Layer 2or Layer 3
Use for cloud bursting, HA, phased application moves . . .
Key
IPSEC VPN (L3)
OpenVPN (L2)
Database
Application
Web
Datacenter
INTERNET
Public
VPC Internet Gateway
Private
VPC Internet Gateway
Public
Private
vpc-928dbffb
10.0.0.0/16
vpc-947f42fd
192.168.0.0/16
Vyatta AMI
(NAT + VPN)
10.0.0.26
EIP: 184.72.121.67
10.0.1.0/16
Vyatta AMI
(NAT + VPN)
192.168.0.92
EIP: 184.72.110.240
192.168.1.0/16
Public IP:
76.74.103.12

## Slide 40: Virtual Networking
INTER VLAN ROUTING, FIREWALL,VPN, AND TRAFFIC INSPECTION
ACCESS
AGGREGATION
CORE
BORDER ROUTER
INGRESS/EGRESS
Database
Application
Web
PHYSICAL
VIRTUAL
INTERNET
Traffic inspected at virtual layer
Reduced latency
Firewall services in all directions
Per-tenant dedicated network controls
On demand provisioning
Network services scale with compute infrastructure
© 2013 Brocade Communications Systems, Inc. Company Proprietary Information
40
Notes: Vyatta provides a new paradigm for true network virtualization, providing robust routing, VPN and firewall functionality within and between hypervisors. The Vyatta approach provides
  Increased throughput
  Reduced latencies
  High Availability (through the hypervisor)
  Increased fault tolerance (through the hypervisor
  In hypervisor security controls
  Application Isolation
  Simplified network topology
Most of all, the Vyatta solution adds agility – allowing system architects to add networking functions that can be deployed with the speed of software.

## Slide 41: Multi-Tenant Cloud Datacenter
Per-tenant network segmentation and security
Highlights
  Firewall
  NAT
  OSPF
  Stateful failover
  Configuration sync
  IPSec or OpenVPN
Use virtual routers to deploy on-demand
VM
1
2
3
VLAN
VLAN
VLAN
ESX
VM
1
2
3
VLAN
VLAN
VLAN
ESX
Physical Network Fabric
Master
Backup
Physical Network Fabric
Virtual Routed Security Gateway

## Slide 42: VyOS in the Public Cloud
Scalable VPN services
  Office to VPC
  User to VPC
  VPC to VPC connectivity
Advanced routing
  Full mesh topologies
  High availability architectures
  Traffic management
IPSEC and SSL
Available in Amazon Marketplace
VM
VM
Amazon Virtual Private Cloud (VPC)
Rackspace Private Cloud (VPC)
Amazon Virtual Private Cloud (VPC)
Customer Data Center

## Slide 43: Software Defined Datacenter
WEB TIER
DB TIER
APP TIER
Dev-App
QA-App
Prod-App
You are already deploying virtual servers
CORE NETWORK
INTERNET
BACKUP NETWORKS
MGMT
NETWORKS
CORE NETWORK
VDI
Backup
Management
FWD DMZ
RA-FWD-IF
RA VPN
REMOTE ACCESS VPN AND VDI TIER FOR ADMINISTRATION
RA-FWD-IF
RA-RWD-IF

## Slide 44: Virtualize the Network
WEB TIER
DB TIER
CORE NETWORK
INTERNET
BACKUP NETWORKS
MGMT
NETWORKS
CORE NETWORK
Backup
Management
FWD DMZ
APP TIER
Dev-App
QA-App
Prod-App
RA-FWD-IF
RA VPN
REMOTE ACCESS VPN AND VDI TIER FOR ADMINISTRATION
RA-FWD-IF
RA-RWD-IF
Now virtualize the network

## Slide 45: Datacenter-In-A-Box
VIRTUAL
PHYSICAL
SERVICE PROVIDER
EQUIPMENT
HIGH SPEED INTERCONNECT TO STORAGE NETWORK
HIGH SPEED BACKPLANE (TB/s)
INGRESS
EGRESS
INTERNET
Template and roll out new datacenters on-demand
Notes: Here is the same network laid out in a 30,000 sq. ft. data center – or the same
Datacenter - virtualized
Solution was architected with blade chassis to provide optimal
  Performance
  Latency
  Redundancy
Blade chassis configured with 4 10G switches for connectivity to backup system and SAN, 2 stacked 1G switches for internet connectivity, 3 half-height blades
Majority of blade traffic travels across chassis backplane.
On average running ~250 VM’s across 3 half-height blades (dual processor dual core 32MB of memory each) for 8 customers and the internal business.
Applications ranges from financial packages, inventory management systems, BI and BPM systems. Largest footprint of VMs were Oracle databases.
At peak average utilization did not exceed 60% across 3 node cluster.
Average ping response 1ms or less.